## Slide 1: TensorTEE: Unifying Heterogeneous TEE Granularity for Efficient Secure Collaborative Tensor Computing
Husheng Han, Xinyao Zheng, Yuanbo Wen, Yifan Hao, Erhu Feng, Ling Liang, Jianan Mu, Xiaqing Li, Tianyun Ma, Pengwei Jin, Xinkai Song, Zidong Du, Qi Guo, Xing Hu

## Slide 2: Background
ZeRO-Offload: Offload the gradients and optimizer states to the CPU while keeping forward and backward computation on NPU
  Zero-offload: Democratizing billion-scale model training (USENIX ATC 21)

## Slide 3: Background
Memory encryption

## Slide 4: Background
Memory encryption
  Mismatched granularity for VN:
    cacheline: 56bit VN per 64B data block CPU TEE
    tensor: Several MBs NPU TEE

## Slide 5: Motivation - 1
Inefficient CPU TEE Computation with Cacheline-Wise Metadata
  Adma optimizer, 3.7x slowdown in TEE
  compute-intensize to memory-intensive
  increased memory access comes from metadata (VN and MAC).

## Slide 6: Motivation - 2
Cacheline-Wise MAC of NPU Leads to Large Storage and Performance Overhead
  predictive execution -> storage overhead remains
  increased granularity (64B to 512B) -> computation stall
tensor-wise MAC with delayed verification
  Tampering can only occur on data but not code
  Tampered data on the NPU cannot leave the NPU chip or memory

## Slide 7: Motivation - 3
Inefficient Data Transfer Protocol

## Slide 8: TensorTEE
Tensor-wise memory protection on CPU
Tensor-wise MAC with delayed verification on NPU
Direct data transfer protocol

## Slide 9: Tensor-wise memory protection
Tensor Management structure
  Tensor-Analyzer 接受CPU核心的内存访问请求,构建和维护运行时meta table的数据结构. 每个条目持有tensor内所有缓存行的共享元数据(VN),消除后续内存请求中的元数据内存访问开销

## Slide 10: Tensor-wise memory protection
Tensor Management structure Location:
          CPU core or Memory Controller
  CPU core (SoftVN):
    acquisition of VNs occurs on critical paths (cache access)
      -> performance down
    waste of entries across multiple cores
  Memory Controller
    Cache interference
    MC receives physical addresses, and their contiguity is limited by the page size
    Long latency for accessing tensor data structures

## Slide 11: Tensor-wise memory protection
1. Cache interference
        the process switches lead to random cache line evictions, disrupting memory access patterns. Additionally, cache prefetchers like stride prefetchers shuffle the access order when the wrong prefetch request is issued.

## Slide 12: Tensor-wise memory protection
2. MC receives physical addresses, contiguity is limited by the page size
  Leveraging virtual addresses from the cores maximizes the utilization of tensor contiguity

## Slide 13: Tensor-wise memory protection
  3. Long latency for accessing tensor data structures
    parallel the data and metadata access

## Slide 14: Tensor-wise memory protection
Writing dataflow
Reading dataflow

## Slide 15: Tensor-wise memory protection

## Slide 16: Delayed Verification for Tensor-Wise MAC

## Slide 17: Delayed Verification for Tensor-Wise MAC
Why can we delay it?
  NPU, being a pure accelerator, lacks the privileged software (like OS) and file I/O abilities.
Ensuring the completion of verification before communication
  tensor poison tracing
    -> poison bit
  verification barrier

## Slide 18: Direct Data Transfer Protocol Implementation
Remote attestation
Communication phase:
  trusted metadata transfer
  direct tensor transfer

## Slide 19: Evaluation
enhanced CPU simulator Gem5
cycle-accurate NPU simulator integrated with Ramulator