## Slide 1: StateMover: Combining Simulation and Hardware Execution for Efficient FPGA Debugging FPGA ’20
王淼
2021-09-28

## Slide 2: Background
FPGA design complexity increasing → debug time ↑
  verification time often takes average 51% of the design cycle
  46% of verification time spent on debugging
FPGA deployment in datacenter increasing

## Slide 3: FPGA Debugging
Simulation
  Full visibility but much slower
  Runs without delays and the spectrum of different possible signal delays on different chips
On-Chip Debug
  Full speed but limited visibility
  Impossible for complex systems

## Slide 4: On-Chip Debugging Techniques
Trace-based
  Full speed
  Stored in on-chip memories
  Only few can be observed for a limited time
  Recompile when modified
Scan-based
  Add additional state access hardware
Readback-based
  No additional hardware
  No instrumentation or modification
  Available on Xilinx FPGAs and on Intel FPGAs
  Requires stopping the design before reading

## Slide 5: StateMover
A checkpointing-based debugging framework
Safely interrupts a design
Moves design state back and forth between FPGA & simulator
  Reads the on-chip state of a design and loads it into simulator
  Full visibility
  Extracts the design state from simulator and writes it back to FPGA
  Full controllability
Combine hardware speed with simulator observability

## Slide 6: StateMover Flow
Add interruption logic (IL) Modules
Run implementation flow in Vivado
Run StateMover (SM) Extract script
Open the SM Console and start a simulation augmented with CSR-SIM

## Slide 7: StateMover Infrastructure

## Slide 8: Safe Interruption Logic
Breakpoint (BP) Logic
  Requests task interruption
  At cycle n, or signal condition y
Task Interruption (TI) Controller
  Safely stop the task
  AXI/Avalon wrappers:
    I/O transactions in-flight complete
    New transactions issued

## Slide 9: User Interface
Simulator
  Load
  Dump
SM Console
  Readback
  Writeback
  Set a hardware breakpoint

## Slide 10: Checkpoint Files for Design State

## Slide 11: State Extraction & Insertion

## Slide 12: State Extraction & Insertion in Simulator
CSR-SIM
  Context Save (dump) and Restore (load)
  Match state element in the simulation model with the corresponding hardware element
    Identifying physical state elements precisely
    Matching hw/sim state element name

## Slide 13: State Extraction in HW
StateConfig: Readback
  Extract the state from Readback file
  Physical to logical (P2L) RAM mapping
    Reconstructs the logical representation of the memories

## Slide 14: State Insertion in HW
StateConfig: Writeback
  Lookup/Calculate location
  Logical to physical (L2P) RAM mapping
  Bitstream manipulation

## Slide 15: Example Session: counter

## Slide 16: StateMover Speed & Scalability
Xilinx Kintex UltraScale KCU105

## Slide 17: Conclusion
A noval FPGA debugging framework
StateMover combines hardware speed with simulator observability
Not capable for BRAM, DSP…
Only for Xilinx Kintex UltraScale series