## Slide 1: FINN: A Framework for Fast, Scalable Binarized Neural Network Inference 2017 ACM/SIGDA International Symposium on Field-Programmable Gate Arrays
王淼
2021-07-29

## Slide 2: Background
Modern CNN: Millions of FP parameters & Billions of FP operations
Accurate classification using one- or two-bit quantization for weights and activations
  small memory footprint -> parameters on-chip -> remove off-chip memory bottleneck
  binary operations in hardware -> higher theoretical peak performance

## Slide 3: FINN
Framework for building scalable and fast BNN inference accelerators on FPGAs
  Millions of classifications per second with sub-ms latency of FINN-generated accelerators
  Compute resources can be scaled to meet a given classification rate requirement
Contributions
  Quantification of peak performance for BNNs on FPGAs using a roofline model
  A set of novel optimizations for mapping BNNs onto FPGA more efficiently
  A BNN architecture and accelerator construction tool, permitting customization of throughput
  A range of prototypes that demonstrate the potential of BNNs on off-the-shelf FPGA platforms
GitHub
  https://github.com/Xilinx/finn

## Slide 4: BNN
FP parameters in CNN can contain a lot of redundant information
BNN: constrain some or all the arithmetic to single-bit values
  Reduce redundancy
  Small drop in accuracy
3 aspects of BNN layers
  Binary input activations
  Binary synapse weights
  Binary output activations
Partial binarization
  One or two components are binary
Full binarization
  All three components are binary
  Only XNOR and popcnt operations are necessary

## Slide 5: How to binarize FP CNN?
BNN express weight and activation by 1 and -1
  Sign function (deterministic)
  Randomly (stochastic)

## Slide 6: Why only XNOR and Popcnt in BNN?
XNOR vs multiplication
Popcount
  Count how many set bits in a bit array
A | B | A XNOR B
1 | 1 | 1
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
A | B | A · B
1 | 1 | 1
1 | -1 | -1
-1 | 1 | -1
-1 | -1 | 1

## Slide 7: XNOR + PopCnt vs MAC
XNOR
PopCnt : ShiftRegister + AND gate
MAC

## Slide 8: Performance compared to CNN
Roofline Models
  FPGA’s compute-bound performance is 66 TOPS for binary operations
  16× higher compared to 8-bit fixed point operations
  53× higher compared to 16-bit fixed point operations
Binarized AlexNet only requires 7.4MB parameters
  Can be kept in on-chip memory
  8-bit FP net : 50MB, off-chip
Reaches 75% of the peak
  Estimated throughput:

## Slide 9: Accuracy–Computation Tradeoffs
A tradeoff between network size, precision and accuracy
  Regular CNN with floating point precision？
  Larger network but BNN?
Experiments on the MNIST dataset shows
  network size increases -> the difference in accuracy decreases
  to achieve the same level of accuracy, BNNs require 2–11× more paras and ops
16x speedup for BNN over 8-bit FP, 2-11x increase in parameters and operations

## Slide 10: Accuracy of BNN
Reference: Binary neural networks: A survey, Haotong Qin et. Al.

## Slide 11: Architecture
Heterogeneous streaming architecture
  ✅ a custom architecture for a given topology
  ❌ scheduling operations on a fixed architecture
Separate compute engines each layer
  communicate via on-chip data streams
Each engine starts to compute as soon as the previous engine starts to produce output
  overlapping computation and communication
  minimizes the initiation interval
Parameters are kept in on-chip memory
Implement in Vivado High-Level Synthesis (HLS) for portability

## Slide 12: BNN-specific Operator Optimizations
Popcount for Accumulation
  128-bit popcount-accumulate requires 376 LUTs and 29 FFs
  128-bit signed-accumulate requires 759 LUTs and 84 FFs.
Batchnorm-activation as Threshold
  abk = Sign(BatchNorm(ak , Θk ))
  Θk = (γk, μk, ik, Bk)
  BatchNorm(ak, Θk) = γk ·(ak −μk)·ik +Bk
  BatchNorm(τk , Θk ) = 0
  => τk = μk − (Bk/(γk · ik))
  2 DSPs, 55 FFs and 40 LUTs vs 6 LUTS
Boolean OR for Max-pooling
  ab = (Max(a1, a2, . . . aY ) > τ+)
  ab = (a1 > τ+)∨(a2 > τ+)...∨(aY > τ+)
  min-pooling (as Boolean AND) and average-pooling (as Boolean majority function)

## Slide 13: Design flow

## Slide 14: MVTU: Matrix–Vector–Threshold Unit

## Slide 15: Convolution: The Sliding Window Unit

## Slide 16: Folding
P-high, S-wide tile per time
  P: the number of PEs
  S: the number of SIMD lanes per PE
X × Y matrix
Fn = X / P as the neuron fold
Fs = Y / S as the synapse fold
F = Fn × Fs as total fold
Example: F = (6 / 3) × (4 / 2) = 4
  Each matrix-vector multiply will take 4 cycles

## Slide 17: Determining Fn and Fs
II : initiation interval
IImax: initiation interval in the lowest layer
Ideal throughput =
  : clock frequency
Fn × Fs =

## Slide 18: Experimental results

## Slide 19: Conclusion
BNNs are particularly well-suited for FPGA implementations
The novel parameterizable dataflow architecture and optimizations presented
  Unprecedented classification rates
  Minimal power consumption and latency
  Offering the flexibility of HLS design entry and the scalability
This technology is eminently suitable for embedded applications requiring real-time response
  Surveillance
  Robotics
  Augmented reality