## Slide 1: Towards a Trusted Execution Environment via Reconfigurable FPGA

## Slide 2: Contents
Problems
Threat Model and Requirements
Design
Proof of concept
Evaluation

## Slide 3: Problems
“TrustZone and SGX have been successfully attacked multiple times”
  Software grand exposure: SGX cache attacks are practical
  CacheKit: Evading memory introspection using cache incoherence

## Slide 4: Problems
PL act as a TEE……？
  physically isolated √
  control mechanisms are hard to attack √

## Slide 5: Threat Model
attacker can take control of the REE and the interfaces to the TEE components
attacker may try to reconfigure the FPGA hardware
  bitstream installed in the FPGA is authentic and cannot be replaced
TEEOD TAs can be malicious
  steal security-sensitive data from other TAs
  attack the host platform by attacking secure devices or accessing
  protected memory regions
D. Cerdeira, N. Santos, P. Fonseca, and S. Pinto, “Sok: Understanding the prevailing security vulnerabilities in trustzone-assisted tee systems,” in 2020 IEEE Symposium on Security and Privacy (SP), pp. 1416–1432,
2020.

## Slide 6: Requirements
Isolation from the REE
Isolation from other TAs
Application management control
Identification and binding
Trusted storage
Trusted access to peripherals
State of the art cryptography
Global Platform, “Introduction to Trusted Execution Environments,” 2018. Accessed: June 2021.

## Slide 7: Design
Design Principles
  avoid sharing hardware and software resources
  principle of least privilege
  well-defined and carefully designed interfaces
Design Overview

## Slide 8: Design——Enclave Life-cycle
Enclave Creation
  list of the available enclaves, loaded TAs
  CA call the TEE Client API to connect with the TEEOD
  (if TA is not loaded) TEEOD copies the target TA binary to a private memory
  TA enters in wait for interrupt state
Enclave Execution
  REE sends information to TEEOD
  TEEOD interrupts TA
  TA reads the message and perform the command
  TA notifies the TEEOD that operation finished and goes back to WFI state

## Slide 9: Design——Enclave Life-cycle
Enclave Destruction
  REE calls the close session function
  TEEOD notifies the TA that the session shall be closed like any other command
  TEEOD clears the memory region of the enclave, hard resets the soft-core
  marks the enclave as available, removes the TA’s UUID from the list, ensuring no information is leaked

## Slide 10: Design——Communication handling
REE applications can exchange information via raw data or shared memory with TAs by leveraging the TEE Client API
CA needs to pass the TEEOD:
  the UUID of the target TA
  the requested message in form of shared registers
  the message type
  the access permissions that the TA has to the message
TEEOD validates the received information, sends the message to
the desired TA through shared registers in case of success
Replies go backwards

## Slide 11: Design——Shared Memory Management
used to transfer large blocks of data
REE CA first allocates the requested memory, provides the address and size of the shared memory area in use
communicates memory pointer and size as normal message

## Slide 12: Proof of concept
TEE Hardware Blocks, TEE Client API, TEE Internal Core API

## Slide 13: Use case: bitcoin wallet
uses a subset of features of the TEE internal core API
  random number generation
  secure storage
  cryptographic primitives
  other cryptographic related operations
functions:
  checks if a master key already was generated
  generates a new master key and corresponding mnemonic, i.e., seed phrase
  generates a new master key from a given mnemonic
  deletes a master key
  signs a blockchain transaction
  obtains the bitcoin wallet address

## Slide 15: Evaluation

## Slide 16: Evaluation
Operation | Time
open session | 54.4 ms
open session of existing TA | 31.1 us
returns a value incremented by one | 201.0 us
outputs a 16-byte array to shared memory | 327.05 us
close session | 40.1 us